## Slide 1
This lesson contains 48 slides and a related video. The first 16 slides are presented here as samples…they deal with a few of the forces of nature as they relate to driving.
Unit 1 – Natural Forces on a vehicle

## Slide 2
T H E D R I V E R S E D G E
slides and videos
I N T E R A C T I V E
Unit 1 – Natural Forces on a vehicle

## Slide 3
- Gravity
- Inertia (energy of motion), momentum
- Kinetic and potential energy
- Friction and centrifugal force
- Factors that affect stopping ability
- Forces of Impact
Laws of Nature
This lesson will deal with how the laws of nature affect your ability to control your vehicle. The laws we’ll consider are:
These forces affect how your vehicle handles so you may react appropriately in emergency situations.

## Slide 4: The Law of Gravity
Let’s first think about gravity.
If you break the laws of nature or misjudge them while driving you may end up losing control and get into a collision.
Gravity is the force that pulls all objects toward the center of the earth. It affects your speed of travel when going uphill and down hill.
Laws of Nature

## Slide 5
When you are driving uphill, the force of gravity is working against you.
You will need to accelerate or change to a lower gear to maintain your speed.
Laws of Nature

## Slide 6
When you are driving downhill, the force of gravity will cause you to go faster and increase your stopping distance.
To control your vehicle you may need to brake or change to a lower gear to slow to a safe speed.
Laws of Nature

## Slide 7
The Law of Gravity and Hill Parking
Laws of Nature

## Slide 8: What are the steps? Downhill with curb
Wheels to right
Shift to neutral
Roll into curb
Shift to Park
Set Parking Brake
When you are parked on an incline, gravity works to pull your vehicle downhill.
To keep your vehicle from rolling, leave your vehicle in low gear or park.

## Slide 9: The Law of Inertia
Objects moving tend to continue moving and objects at rest tend to remain at rest unless acted upon by some outside force.
While driving, inertia keeps your vehicle moving unless it is acted upon by something to slow or stop it. Braking, the road surface, a fixed object, or another vehicle will all interrupt or stop the force of inertia.
Laws of Nature

## Slide 10: The Law of Inertia
This force causes your body and loose objects in your vehicle to keep moving forward when your vehicle suddenly slows or stops.
You may be injured because of the inertia and the momentum of loose objects that become airborne during a sudden stop.
Laws of Nature

## Slide 11: The Law of Inertia
Wearing a seatbelt while driving will stop the forward momentum of your body if you have a collision. It will prevent you from hitting the windshield, steering wheel, and other parts of the interior of your vehicle.
If you are hit from behind while stopped, your head tends to stay in place due to inertia while the rest of your body is pushed forward by the seat. This causes whiplash. Using your headrest minimizes injuries.
Check to see
that it is
properly adjusted
Laws of Nature

## Slide 12: Potential Energy
Potential energy is the energy that an object possesses because of its position or form.
For example, a book on the edge of a table has the “potential” energy to fall to the floor.
However, a book that is already on the floor does not have this potential energy.
. . . now, applying this to vehicles
Laws of Nature

## Slide 13: Potential Energy
When you are parked on a hill, gravity also causes your car to have potential energy.
This energy is converted to kinetic energy (motion) if it brakes loose and rolls down the hill.
There is also potential energy built up in the components of your car’s suspension that may cause you to swerve out of a turn.
. . . let's now think about kinetic energy
Laws of Nature

## Slide 14: Kinetic Energy
Kinetic energy is the energy a body possesses because it is in motion.
As you increase your driving speed, both your body and your vehicle acquire kinetic energy (motion) which eventually must be:
a) absorbed by your brakes, engine compression forces, or other friction in a controlled stop.
b) absorbed by your body, and the objects you hit if you are involved in a crash.
Laws of Nature

## Slide 15: Kinetic Energy
Kinetic energy is the energy a body possesses because it is in motion.
The kinetic energy of your body while it is in motion, of loose objects in the car, and the car itself, all increase with weight and the square of your speed so that:
- if you increase your speed from 10 mph to 20 mph you are dealing with four times the amount of kinetic energy, and if you increase your speed from 10 mph to 50 mph you have to deal with 25 times the amount of kinetic energy.
Laws of Nature

## Slide 16: Kinetic Energy
Kinetic energy is the energy a body possesses because it is in motion.
The kinetic energy of your moving vehicle determines your ability to stop the car. In addition to the distance traveled due to your reaction time, your stopping distance will be:
- five times further if you increase your speed from 10 mph to 20 mph.
- 25 times further if you increase your speed from 10 mph to 50 mph.
. . . let's now think about kinetic energy & gravity
Laws of Nature

## Slide 17: Kinetic Energy
Kinetic energy is the energy a body possesses because it is in motion.
Gravity decreases your kinetic energy when you are driving uphill, making it easier to stop. When going downhill, it increases, making it more difficult to stop.
Braking to a stop converts kinetic energy into heat energy in your brakes by the friction that is generated.
But, if you and your vehicle are involved in a collision, the kinetic energy is still converted into heat energy, but not through your brakes…you and your car must absorb that energy! (ouch)
. . . let's now think about momentum
Laws of Nature

## Slide 18: Momentum
Momentum is the force of a moving object. The momentum of an object is proportional to its weight and speed.
When driving, you and you vehicle acquire a momentum which is proportional to the weight of your vehicle and its speed. Increasing your speed from 10 to 20 mph, doubles your car’s momentum. From 10 to 50 mph, you increase it 5 times.
For example, a baseball traveling at 10 mph has more momentum (force) than a ping pong ball traveling at the same speed.
Laws of Nature

## Slide 19: Momentum
When in a crash, the momentum and kinetic energy of your vehicle must be absorbed, which results in heat, the deformation of your vehicle, and possibly injury to your body.
When you make a controlled stop, the momentum of your vehicle must be overcome by (a) the friction force of your brakes, (b) the friction force between your tires and the road, and (c) the compression force of your engine.
Laws of Nature
Momentum is the force of a moving object. The momentum of an object is proportional to its weight and speed.