## Slide 1
T H E D R I V E R S E D G E
slides and videos
Unit 5 – Vehicle Maintenance
I N T E R A C T I V E
Partial lesson
18 of 48 slides

## Slide 2
Vehicle Maintenance

## Slide 3
Vehicle Maintenance
This lesson will focus upon things the average person, with a little knowledge and desire, can do to help maintain their car in good operating condition.
There are many things that you can do to keep your car in good condition, but there are some things that need to be left to mechanics.

## Slide 4: What You Can Do
Check your tire pressure
Rotate your tires
Check and change your oil
Check and fill various fluid levels
Replace air filter, fuses
Changing bulbs and lights
Change a flat tire, jump start a car
Vehicle Maintenance

## Slide 5: Checking Tire Pressure (check at every fuel fill up)
To check your tire pressure first unscrew the air cap off of the tire rim.
Then use a pressure gauge to check your tire pressure and compare it to the sticker on the inside of the door.
If your tire pressure is low, you should add air to your tire as recommended.
Vehicle Maintenance
What
do you
know
about
checking
tire
pressure?

## Slide 6: Checking Tire Pressure
Vehicle Maintenance
It is also a very convenient way to check your tire pressure.
Some newer cars will alert you when your tire pressure is low by displaying it on the dash board.

## Slide 7: Tire Rotation (usually about every 5000 miles)
Tire rotation will allow your tires to last much longer.
Refer to your vehicles users manual for the proper tire rotation patterns and for how often they should be rotated.
Vehicle Maintenance
For you to do this job you’ll need these . . .
What
do you
know
about
tire
rotation?

## Slide 8: Checking Your Oil
To check your oil, first pop the hood.
Find your dipstick, pull it out and wipe it off with a rag.
Reinsert it. Then pull it back out and check the level of oil on the dipstick.
Add oil if you are 1 quart or more down from “full”
Vehicle Maintenance
What
do you
know
about
checking
your
oil?

## Slide 9: Adding oil
First locate the oil fill cap under the hood.
Remove the oil fill cap.
Add the proper type of oil according to the owners manual for your car.
(an oil funnel will keep drips to a minimum)
Vehicle Maintenance
How often should you
change the oil?

## Slide 10: When To Change Your Oil
About every 3,000 - 5,000 miles or 3 months
See owners manual for specifics
Vehicle Maintenance

## Slide 11: Checking Brake Fluid
To check and add brake fluid first locate the brake fluid reservoir under the hood.
Vehicle Maintenance
Remove the cap off the brake fluid reservoir.
If the fluid level is under the minimum, add the recommended brake fluid to the reservoir.
What
do you
know
about
checking
the brake fluid?
What are warnings
of bad brakes?

## Slide 12: Bad Brakes warning
If your brake warning light is on and your parking brake is not set then you may have a problem with your braking system
If you notice a squealing noise when braking it could mean your brake pads are worn and need replacing.
Vehicle Maintenance

## Slide 13: Checking Windshield Washer Fluid
To check your windshield washer fluid first locate the washer fluid reservoir.
Vehicle Maintenance
Then pop the cap off of the windshield washer fluid reservoir.
If the fluid level is looking low top it off with washer fluid.
What is the
usual
color
is the
windshield
washer fluid?

## Slide 14: Engine Temperature
You should frequently check your temperature gauge while driving.
Vehicle Maintenance
If your car begins to overheat, especially in hot weather you should turn on the heater and fan on high; if the engine temperature does not soon lower you should pull over and let your car cool down.
Gauge reads hot

## Slide 15: Engine Temperature
Vehicle Maintenance
After the engine has safely cooled down (it may be an hour) remove the radiator cap.
If the fluid level is low add a 50/50 mix of anti-freeze and water.

## Slide 16: Know your fluids
If you notice fluids under your car where it is normally parked, than you most likely have a leak which needs to be professionally checked out.
Vehicle Maintenance
Motor oil: check
under engine
Transmission fluid: check under
car…back part of engine
Coolant: check
water pump,
radiator or hose
Power steering
fluid: check system
Water: usually
condensation

## Slide 17: Changing bulbs
Vehicle Maintenance
If the fuse is not the problem it could be a burned out bulb.
It can be a simple or challenging procedure; see owners manual for bulb type.
Best to bring old bulb with you to auto parts store.

## Slide 18: Things better left to professionals (unless you’ve had special training and have access to the proper equipment)
Vehicle Maintenance
Major tune-ups: often require technical equipment
Engine problems: noises, fluid leaks; odors, broken belts, hoses, vibrations
Transmission problems
Rotating tires
Brake jobs
Radiator flushing
Air conditioning
Exhaust / steering system
Most electrical problems

## Slide 19: Gasohol (ethanol)
Gasohol is a mixture of 90% gasoline and 10% ethanol.
Ethanol is often made from corn by-products.
Gasohol has a higher octane and anti-knock properties than gasoline.
Gasohol burns slower and cooler than gasoline making it more economical and it results in reduced emissions.
Other considerations
What
do you
know
about ethanol
(Gasohol)

## Slide 20: Gasohol (ethanol)
Other considerations
Gasohol is more expensive and energy intensive to produce. Not suitable for all cars.
It can damage rubber seals and diaphragms in cars that are not compatible with it.
It is also toxic and corrosive; check owners manual to see if it is not recommended.